## Slide 1: Process Control and instrumentation

## Slide 2: Contents
Introduction to Process Control

## Slide 3
The driver must have a goal or objective; normally, this would be to stay in a specific lane. First, the driver must determine the location of the automobile, which she does by using her eyes to see the position of the automobile on the road. Then, the driver must determine or calculate the change required to maintain the automobile at its desired position on the road. Finally, the driver must change the position of the steering wheel by the amount calculated to bring about the necessary correction. By continuously performing these three functions, the driver can maintain the automobile very close to its desired position as disturbances like bumps and curves in the road are encountered
person driving an automobile –

## Slide 4: the simple heating system
The house, in a cold climate, can be maintained near a desired temperature by circulating hot water through a heat exchanger. The temperature in the room is determined by a thermostat, which compares the measured value of the room T a desired range, say 18 to 22°C. If the temperature is below 18°C, the furnace and pump are turned on, and if the temperature is above 22°C, the furnace and pump are turned off. If the temperature is between 18 and 22°C, the furnace and pump statuses remain unchanged. A typical temperature history in a house in which shows how the temperature slowly drifts between the upper and lower limits. It also exceeds the limits, because the furnace and heat exchanger cannot respond immediately. This approach is termed "on/off" control and can be used when precise control at the desired value is not required. We will cover better control methods, which can maintain important variables much closer totheir desired values.

## Slide 5: Introduction to Process Control
In any chemical engineering - extensively used equipment are reactors, distillation column, heat exchangers, pumps, compressors, evaporators etc….
To constitute a chemical plant –need to combine few of these equipment.
Objective of a chemical plant –to produce product in a most economical way using the available resources of energy and received raw materials
To encounter these objects –need to meet some requirements are
Safety – reactor (100 psig pressure – to maintain & operate below - external intervention )
Product specifications – desired quality & quantity
Environmental requirements – state and federal laws such as concentration of chemicals, waste water discarding, S02 concentration.
Chemical Plant
Raw materials
Product

## Slide 6
4. Operational constraints – certain constraints are maintained to operate a unit process such as Distillation column - flooded
Tanks – Overflow or go dry
Catalytic reactor – temperature overshot
5. Economic consideration – Minimum operating cost, Maximize profit
To meet up & maintain all these requirements we require external interventions – i.e. called control system.
The control system suppress the following issues such as
The influence the external disturbance
The stability of a chemical process
The performance of a chemical process

## Slide 7: Influence the external disturbance
Agitated heating tank /system:
Objective - To maintain liquid temp at desired temp T = TR, heat i.e., h =hd
T, h
W, T
Heater, q
W, Ti
Agitator
Ti – Initial temp of stream (inlet)
TR – Desired temp
W- constant mass flow rate, mass/time
T- temp in the tank
C- specific heat of fluid
h – height of the liquid
Notes: A liquid stream at temperature Ti is available at a constant flow rate of w in units of mass/time. It is desired to heat this stream to a higher temperature TR. The fluid flows into well agitated tank equipped with a heating device. It is assumed that the agitation is sufficient to ensure that all fluid in a tank will be at the same temperature, T. Heated fluid is removed from the bottom of the tank at the flow rate w as the product of this heating process. Under these conditions, the temp of the effluent fluid is same as that of the fluid in the tank. The specific heat of the fluid C is assumed to be constant, independent of temp.

## Slide 8: Steady state
Start up process – reaches steady state
Energy balance eqn. at S S,
qs =wC (Ts-Tis)
qs – heat input tank at S S
If Tis – anticipated inlet temp to the tank.
For satisfactory design, SS temp of effluent stream Ts must equal TR . Hence
qs =wC (TR-Tis)
thermocouple
Td
controller
Notes: A process is said to be at steady state when none of the variables are changing with time. At the desired steady state, an energy balance around the heating process is qs =wC (Ts-Tis).