## Slide 1: Advanced Computer Networks (ACA)
Prof. Santosh K C
Asst. Prof.
CSE Dept.
B.I.E.T.
Davangere-04

## Slide 2: Pipeline Review
1
0
1
Read address
Instruction memory
Instruction
[31-0]
Address
Write data
Data memory
Read data
MemWrite
MemRead
1
0
MemToReg
4
Shift left 2
Add
ALUSrc
Zero Result
ALU
ALUOp
Instr [15 - 0]
RegDst
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Add
Instr [15 - 11]
Instr [20 - 16]
0
1
IF/ID
ID/EX
EX/MEM
MEM/WB
Control
M
WB
WB
P C
1
0
PCSrc
Sign extend
EX
M
WB

## Slide 3: Our examples are too simple
2
Here is the example instruction sequence used to illustrate pipelining on the previous page
lw $8, 4($29)
sub $2, $4, $5 and $9, $10, $11 or $16, $17, $18 add $13, $14, $0
The instructions in this example are independent
Each instruction reads and writes completely different registers
Our datapath handles this sequence easily
But most sequences of instructions are not
independent!

## Slide 4: An example with dependences
3
Read after Write dependences
sub $2, $1, $3 and $12, $2, $5 or $13, $6, $2
add $14, $2, $2 sw $15, 100($2)
Dependences are a property of how the computation is expressed

## Slide 5: An example with dependences
and | $12, | $2, | $5
or | $13, | $6, | $2
add | $14, | $2, | $2
sub $2, $1, $3
sw $15, 100($2)
There are several dependences in this code fragment
The first instruction, SUB, stores a value into $2
That register is used as a source in the rest of the instructions
This is no problem for 1-cycle and multicycle datapaths
Each instruction executes completely before the next begins
This ensures that instructions 2 through 5 above use the new value of $2 (the sub result), just as we expect.
How would this code sequence fare in our pipelined datapath?
4

## Slide 6: Data hazards in the pipeline diagram
5
Clock cycle
1 2 3 4
5 6 7 8
9
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
sub $2, $1, $3
and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $15, 100($2)
The SUB does not write to register $2 until clock cycle 5 causeing 2 data hazards in our pipelined datapath
The AND reads register $2 in cycle 3. Since SUB hasn’t modified the register yet, this is the old value of $2
Similarly, the OR instruction uses register $2 in cycle 4, again
before it’s actually updated by SUB

## Slide 7: Things that are okay
6
Clock cycle
1 2 3 4
5 6
7
8
9
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB
sub $2, $1, $3
and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $15, 100($2)
The ADD is okay, because of the register file design
Registers are written at the beginning of a clock cycle
The new value will be available by the end of that cycle
The SW is no problem at all, since it reads $2 after the SUB finishes

## Slide 8: One Solution To Data Hazards
7
sub $2, $1, $3
and | $12, | $2, | $5
or | $13, | $6, | $2
add | $14, | $2, | $2
sw $15, 100($2)
Since it takes two instruction cycles to get the value stored, one solution is for the assembler to insert no-ops or for compilers to reorder instructions to do useful work while the pipeline proceeds
A software solution to data hazards
sub | $2, | $1, | $3
sll | $0, | $0, | $0
sll | $0, | $0, | $0
and | $12, | $2, | $5
or $13,
add $14,
sw $15,
$6, $2
$2, $2 100($2)

## Slide 9: A fancier pipeline diagram
8
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or | $13, $6, $2
add | $14, $2, $2
sw | $15, 100($2)
1 2 3 4
Clock cycle
5 6 7
8
9

## Slide 10: Forwarding
9
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
1 2 3 4 5
6
7
Since the pipeline registers already contain the ALU result, we could just forward the value to later instructions, to prevent data hazards
In clock cycle 4, the AND instruction can get the value of $1 -
$3 from the EX/MEM pipeline register used by SUB
Then in cycle 5, the OR can get that same result from the MEM/ WB pipeline register being used by SUB
Clock cycle

## Slide 11: Forwarding Implementation
Forwarding requires …
Recognizing when a potential data hazard exists, and
Revising the pipeline to introduce forwarding paths …
We’ll do those revisions next time
10

## Slide 12: What about stores?
11
DM
Reg
Reg
IM
DM
Reg
Reg
IM
add $1, $2, $3
sw $1, 0($4)
DM
Reg
Reg
IM
DM
Reg
Reg
IM
add $1, $2, $3
sw $4, 0($1)
Two “easy” cases:
1 2 3 4 5 6
1
2
3
4
5
6